## Slide 1: AUTOCAD 2D - I
MODULE – 1
Introduction to Drawing Tools

## Slide 2: Learning Objectives
Identify and describe the use of engineering drawing equipment
Recognize different methods of laying out engineering drawing papers.
Demonstrate the use of scales.
Produce a simple drawing paper layout including border and title block.

## Slide 3: Introduction
What is AutoCAD 2D ?
Computer-aided design (CAD), is the use of computer technology for the process of design and design-documentation.
CAD often involves more than just shapes.
CAD may be used to design curves and figures in two-dimensional (2D) space; or curves, surfaces, and solids in three-dimensional (3D) space.
CAD is an important industrial art extensively used in many applications, including automotive, shipbuilding, and aerospace industries, industrial and architectural design and many more.
CAD is also widely used to produce computer animation for special effects in movies, advertising and technical manuals.

## Slide 4
2D ( 2 DIMENSIONAL )
2D is something with 2 dimensions, which are length and width
3D ( 3 DIMENSIONAL )
3D is something with 3 dimensions, which are length, width, and depth.

## Slide 6: Technical Drawing
Every product we have today (e.g. cars, houses, machines, etc…), began as an "idea" in some person's head. Before these "ideas" became products, they had to be drawn on paper.

## Slide 7: Manual Instruments

## Slide 8: Manual Instruments

## Slide 9: Free - hand Sketch
To prepare a drawing, one can use manual drafting instruments or computer-aided drafting (CAD).
If the drawing is made without either manual instruments or CAD, it is called a freehand sketch.

## Slide 10: Drawing Instruments
The following instruments are essential and should be
available to produce a good quality technical drawing.
Drawing Boards
T-Square
Set Square
Pairs of Compasses
Protractor
Ruler
Drawing pencils
Eraser
Circle template

## Slide 11: Drawing Boards
Drawing Boards can range from simple boards to complicated drawing machines that would be used in engineering drawing office.
The surface of the board should be dusted and smooth.

## Slide 12: T - Square
T- Square is composed of a long strip, called the blade.
It is placed on the drawing board and provides a constant horizontal edge.

## Slide 13: SET SQUARE
Set Squares are best made from transparent plastic.
The two standard set squares that are commonly used are 30/60 and 45/45 degrees triangles

## Slide 14: Compasses
Pencil Compass
Pencil compasses which are used to draw circles. Circles up to 300 mm diameter are drawn using a large radius compass.

## Slide 15
Spring bow compass
Spring bow compass which is used to draw circles of 50 mm diameter or less.

## Slide 16: Protractor
Protractors measure angles other than those obtained by the set squares and found in half circle or full circle types.

## Slide 17: Ruler
A 300 mm ruler with one edge marked in centimeters and millimeters is used.
In a fully equipped drawing machine, horizontal and vertical rulers with graduations in mm or inches are attached to the drafting head.

## Slide 18: Drawing Pencils
Pencils have nine grads of hardness
from H to 9H
seven grades of softness from B to 7B

## Slide 19: Eraser
Erasers are available in different hardness and are used to erase pencil work.
The common eraser used is a block-shaped vinyl eraser.

## Slide 20: Circle template
Circle templates are useful for drawing small circles quickly and to join lines with a radius.

## Slide 21: Drawing Paper Sizes of the drawing paper
Drawing paper is available in ‘A’ series, ‘B’ series, and rolls of the International Organization for standardization (ISO), but series ‘A’ is preferred.
Paper sizes for series ‘A’ are based on the A0 size, which has an area of 1 square meter.
An A0 size sheet can be divided up evenly into the various other sizes (A1, A2, A3, A4…) simply by halving the sheet on the long side in each case.

## Slide 22: Scales
In order to produce drawing showing components in detail or as plans it is often necessary to use a scale.
This can increase the size of the drawing in comparison to the real size of the component.
Some of the recommended scales are listed below:
Enlargements scales: 2:1 20:1 50:1 10:1
Full (same) size: 1:1
Reduction scales: 1:2 1:10 1:20 1:100

## Slide 23: Layout of the drawing paper
Drawing sheets of all sizes have standard layout.
It is usual for each sheet to be provided with a drawing frame a short distance from the edge of the paper
Each drawing sheet has to be provided with a title block which represents the general information source for a drawing.
It is normally placed in the bottom and at least contains the title of the drawing, the name of the draftsman, the scale, and the date.

## Slide 25: Line type

## Slide 26
Leader lines: Leader lines are thin continuous lines that point to features on an engineering drawing with an arrowhead. They are accompanied by a dimension or local note that specifically describes that feature.
Projection lines: Projection lines are thin continuous parallel lines that project out from a drawing to help describe a component. They are drawn two at a time with a dimension and a dimension line between them.

## Slide 27
Dimension Lines: A dimension line is a thin continuous line that describes a component on an engineering drawing. It has one or two arrow heads and always refers to a dimension.
Hatching is the use of fine, parallel lines drawn closely together, often rapidly drawn, to create the illusion of shade or texture in a drawing.
Distance may be varied to allow more or less white space between the lines, or lineweight varied to thicken the darkness of the lines.
Often used in pencil sketching and in pen-and-ink drawing.

## Slide 28
A drawing needs to give the person making the component all the information they need. Dimensions and notes are written on the drawing. Lines are used to explain how these dimensions and notes relate to the object. This is called 'dimensioning a drawing'.
Projection lines are thin continuous lines that come away from the drawing at the feature being sized.
Dimension lines are thin continuous lines with an arrowhead on both ends. The dimensions are placed on top of the dimension line. Dimension lines should not be placed over the outline of the drawing unless there is no other option.
Leader lines are thin continuous lines that indicate where dimensions, notes and item numbers apply. The leader line should terminate with an arrowhead at the feature end and a short horizontal line (approx 5 mm) at the dimension end.

## Slide 29: DIFFERENT LINES IN A DRAWING

## Slide 30: Technique of Lettering
Printing increase the information that is provided on a drawing.
Printing must be clear and neat so that it is easy to read. Use guide lines 5 mm apart as illustrated in Fig.

## Slide 31
These guide lines can be used to make sure that all letters and numbers have the same size.
Always print using capital letters.
All letters and numbers should touch the top and bottom guide lines.

## Slide 32: ACTIVITIES
Draw the objects shown below in full size using different drawing tools such as compasses, set squares and tee square. Use an A3 sheet to create the drawing with the same layout shown below.